This prototype is a conceptual and computational exploration of vesicle diffusion inside a cellular geometry, created after reviewing the paper provided by the professor. The goal was to quickly implement a testbed that:
- Simulates vesicle diffusion in a constrained spatial mesh
- Identifies local vesicle-triangle overlaps efficiently
- Prepares the groundwork for eventual tetrahedral (3D) extension

## Design Overview
The simulation simplifies the full 3D cell into a 2D triangular mesh (analogous to a tetrahedral volume in 3D), and vesicles are modeled as moving circular particles with discrete sample points on their membrane.
Key components include:
- Cell: generates a 2D hexagonal triangle mesh
- Triangle: stores geometry and outward normals for side tests
- Vesicle: holds the center, radius, and sample points
- Vesicles: manages multiple vesicles and their diffusion
- Visualizer: uses Vispy to render the entire system interactively

## Method: Overlap Detection via Vectorized Side Test
For each vesicle:
- A number of sample points are placed on its membrane (n = 8)
- The algorithm uses vectorized 2D side-tests to check whether any sample lies inside a triangle
- Triangle normals are precomputed; the test computes:
dot(P−Vi​,ni​)≤0∀i=1,2,3
If any point lies inside, the triangle is considered overlapping / occupied.
This structure is:
- Fully vectorized using NumPy broadcasting
- Easily extendable to 3D tetrahedrons (by testing against 4 face planes)
- Ready for GPU acceleration using CuPy or PyTorch if needed

## Diffusion Model
Diffusion is modeled as Brownian motion:
Δx=2DΔt​⋅ξ
- D = vesicle-specific diffusion coefficient
- Δt = timestep
- ξ = Gaussian random direction vector
Vesicle movement is rejected if the new position overlaps with an already occupied triangle (simple exclusion rule).

## Performance
Although the prototype is simple, it is:
- Efficient due to NumPy vectorization
- Accurate enough for conceptual validation
- Structured to allow modular extension to 3D geometry